## Slide 1: Comp 150/EE194: Introduction to VLSI CAD
Spring 2017Tufts University
Instructor: Joel Grodstein
joelg@eecs.tufts.edu
Discrete-event simulation

## Slide 2: What we'll cover today
Event-oriented simulation
What is simulation?
  Build a virtual model of something.
  Run the model with some inputs (this is the simulation part!)
  See if the model's outputs match what you expect
Simulation is a big part of validation – testing whether your design works or not.

## Slide 3: Why do we care
How many of you have ever written a non-trivial computer program?
How many of you always have your programs work perfectly the first time?
Designing things is easy.
  Designing things that work is not so easy!
We all agree that validating stuff we design is important. But why build virtual models of it?
  Why not just build the real thing, try it out and iterate?

## Slide 4: What are some things to simulate?
A virtual world (a.k.a. a video game)
  Why? Because it's fun.
An airplane
  Flight simulation: e.g., to train pilots
A pacemaker
  Because trying out your first version in a real human is not really a good idea
A VLSI chip
  Because building the first one costs several $M
A bacteria
  Because they can be dangerous and expensive

## Slide 5: A few more things to sim
A few published papers:
  Simulate the effect of various air-traffic control policies on congestion and safety (Conway 2006)
  Crime Analysis. A realistic virtual urban environment, populated with virtual burglar agents (Malleson 2010)
  Simulating the smart power grid. GECO: Global Event-Driven Co-Simulation Framework for Interconnected Power System and Communication Network, 2013.

## Slide 6: What will we cover today?
Discrete-event simulation: how it works
Discrete-event simulation as a way to use multi-core processors
Example: simulating a VLSI network
Example: simulating a cure for cancer

## Slide 7: Continuous vs. discrete
Models can be continuous or discrete. Who remembers the difference?
  Continuous: mostly differential equations. Accurate but slow.
  Discrete: interesting events happen at distinct times, and nothing noteworthy happens in between. Big speedup – if you can live with this model.
George Box: all models are wrong; some are still useful.
We will focus on discrete-event models.

## Slide 8: Simplest of gates: a buffer
Input=0 → output=0. Input=1 → output=1.
A
B
Now let's add some delay to it.

## Slide 9: Buffer with delay
The output is simply a delayed copy of the input. Period.
The Δt might be different for different buffers.
  Similar to a parameterized object.
A
B
time delay of 3 seconds
3

## Slide 10: Next simple gate: an inverter
Input=1 → output=0. Input=0 → output=1. Delay = (e.g., 3).
A
B
3
A
B

## Slide 11: AND gate
Input=1 → output=0. Input=0 → output=1. Delay = (e.g., 3).
A
B
3
A
B
C'
C

## Slide 12: What if we have a big network?

## Slide 13: Events
For big networks, we cannot deal with pictures of waveforms. Why?
  Computers don't store pictures real efficiently
  We want to deal with objects and algorithms
Three types of objects:
  A gate (each instance of AND, OR, INV, etc).
  A node (what we've called A, B, C, etc). It has a value at the current time
  An event. I.e., a given node rising or falling at a given time.

## Slide 14: AND gate with events
Input=1 → output=0. Input=0 → output=1. Delay = (e.g., 3).
A
B
3
A
B
C'
C
A=1@3
A=0@5
B=1@4
B=0@8

## Slide 15: Simulating our AND gate
Let's do a simulation.
A
B
3
A=1@3
A=0@5
B=1@4
B=0@8
Current time
0
Pending events
C
0
0
0
3
1
1 & 0 → 0
C=0@3

## Slide 16: Simulating our AND gate
Let's do a simulation.
A
B
3
C=0@3
A=0@5
B=1@4
B=0@8
Current time
0
Pending events
C
1
0
0
3
C is already 0, so this event does nothing!

## Slide 17: Simulating our AND gate
Let's do a simulation.
A
B
3
B=1@4
B=0@8
A=0@5
Current time
3
Pending events
C
1
0
0
4
1
1 & 1 → 1
C=1@7

## Slide 18: Simulating our AND gate
Let's do a simulation.
A
B
3
A=0@5
B=0@8
C=1@7
Current time
4
Pending events
C
1
1
0
5
0
0 & 1 → 0
C=0@8

## Slide 19: Simulating our AND gate
Let's do a simulation.
A
B
3
C=1@7
C=0@8
B=0@8
Current time
5
Pending events
C
1
1
0
7
0
This change on C does not have any fanout

## Slide 20: Simulating our AND gate
Let's do a simulation.
A
B
3
B=0@8
C=0@8
Current time
7
Pending events
C
1
0
1
8
0
0 & 0 → 0
C=0@11

## Slide 21: Simulating our AND gate
Let's do a simulation.
A
B
3
C=0@8
C=0@11
Current time
8
Pending events
C
1
0
0
8
0
This change on C does not have any fanout

## Slide 22: Simulating our AND gate
Let's do a simulation.
A
B
3
C=0@11
Current time
8
Pending events
C
0
0
11
0
The value on C does not change
DONE!

## Slide 23: More practical consequences
Trends in functional validation: an industry study, 2014
  Large survey (1886 good responses) by Mentor graphics
Conclusions:
  Average 57% of time spent on verification
  Most projects spend 60-70% of their time.
  Average 11 val engineers, 10.1 design eng per project.
  2007-2014 CAGR for DE=4%, VE=12% (and DE spending 50% of their time on val).

## Slide 24: SWARM
SWARM (Prof. Daniel Sanchez, MIT).
  Seminar in Halligan last December
What problem did SWARM solve?
  Intel keeps selling us multi-core CPUs; 64 processors with 2B instruc/second, rather than one CPU with 100B instruct/second.
  Why is this a problem?
  Because parallel programming is really hard. Breaking one big problem into 64 little problems that are mostly independent is not the way our brains work.

## Slide 25: SWARM
SWARM part 1:
  Designed a chip that would run parallel DES really well
  Mostly just a standard multi-core CPU with some secret sauce
SWARM part 2:
  Showed you can turn various graph and database algorithms into DES
  I.e., DES is used for more than just DES!

## Slide 26: Curing cancer
Well, perhaps not today.
One interesting strategy: re-purposing bacterial chemotaxis.
Why are we talking about curing cancer?
  Well, because most people would agree it's an important problem
  More to the point, because we can easily simulate our strategy

## Slide 27: What is bacterial chemotaxis?
Bacteria, like every living thing, need to find food
E.coli has sensors that can sense the presence of sugar.
  Based on these sensors, it steers itself towards the sugar
Big picture, no problem – but…
  E.coli is too small to swim in a straight line; it keeps getting hit by particles big enough to knock it off course (i.e., it needs frequent course correction).
  E.coli is too small to sense a spatial gradient (the difference in concentration between its front & back is often less than 1 molecule)

## Slide 28: So what's an E.coli to do?
while (1)
  note the sugar concentration level & remember it
  pick a random direction
  swim for a bit
  if (current concentration < old concentration)
    pick a new random direction
That's it:
  Substantial oversimplification compared to real E.coli, but it captures the main idea
  The real one uses the difference between a fast reaction (phosphorylation) and a slower reaction (methylation) to "remember" the old concentration.

## Slide 29: But how does that cure cancer?
Tumor cells are typically more acid and more dense than surrounding tissue
  Sensors can recognize this
  We can use recombinant DNA techniques to graft new sensors into E.coli, so that it hunts down tumor cells.
Reprogram it again to release lethal chemicals when it finds the cancer cell.
Result: we have a tumor-hunting bacteria that reproduces like crazy kills on contact.
References:
  Environmentally-Controlled Invasion of Cancer Cells by Engineered Bacteria, JMB 2006.
  Synchronized cycles of bacterial lysis for in vivo delivery, Nature 2016.

## Slide 30: Our model
tumbler
tumbler
accumulator
accumulator
sensor
delay line
decider
Δx
Δy
x
y
sugar_level
old_sugar_level
do_tumble

## Slide 31: Simulation runs fine
The E.coli uses our algorithm.
The algorithm works perfectly
  Admission: I did not get it right the first time!
So why should we not expect the Nobel Prize anytime soon?
Class exercise:
  Break into small groups
  Play the game: how many things did the professor do wrong?

## Slide 32: What's wrong with our sim?
Our model does not match the actual E.coli chemotaxis. We've proved that our model can find a target, but not that the real organism can.
We've not even tried to model what happens when the bacteria hits the tumor.
Even if the bacteria destroys the tumor: who will destroy the bacteria?
Conclusion of the 2006 paper: ??